## Slide 1: AAA in Arrowhead
Hegedűs Csaba (hegeduscs@aitia.ai)
Plósz Sándor
Pál Varga
Gábor Soós
AITIA Inc.
Budapest University of Technology

## Slide 2: Security requirements - CIAAA
Confidentiality:
  Encryption, proper key exchange
(Message) Integrity:
  Encryption, digest or signature
Authenticity:
  Parties are able to verify identify of each other
Availability:
  Resource planning, redundancies
Accountability:
  Logging
  Governance of resources and information
Notes: Also:
We have to differentiate between private data and that of public interest.
We have to protect the systems that provide such data approprietly.

## Slide 3: Threats in IIoT

## Slide 4: A - A – A within Arrowhead
Authentication
  Identity verification (@ Core Systems and @ other App. Systems)
Authorization
  Admission into Local Cloud (when System wakes up):
    does this System belong to us?
    „Bootstrapping mechanism” is required, see Future Work
  Access rights management (are you entitled to use that?)
    For local scenarios: intra-Cloud authorization rules
    For inter-Cloud authorization
  Admission control (per transaction/session; at Service Provider side)
    The final release of service data is the right of the Service Provider!
Accounting
  Services consumed/session start-end with timestamps
  This should be a Core System (e.g. Historian?)
  Under design (within G3.2)

## Slide 5: Previous solution(s)
Ticketing-based Authorization: uses UDP and immutable tickets
Only an authentication solution, not authorization!
System A
System B
AAA System
Radius Server
1. Request token (+authentication)
2. Check credentials
3. Check response
5. Return token
6. Access request
4. Generate token
7. Request token validation
8. Validation response
9. Access response

## Slide 6: Shortcomings of RADIUS-based ticketing
Authentication info sent unencrypted
Communication overhead (authentication server always in the loop)
Token does not bind any identity – can be captured and re-used (immutable ticket sent over UDP)
Not flexible and not scalable

## Slide 7: Shortcomings of Generation 3.0
AuthorizationControl service:
  Stores X.509 certificate CN-s partially, retrieves CN on request
  The Service Provider is only capable of:
    Verifying whether the inbound certificate CN overlaps with the stored CN
  This solution can be bypassed very easily:
    Generate a self-signed certificate with a CN that matches the stored CN
    The Provider cannot verify the certificate chain from the AuthControl service
    Unless it has root cert-s for all vendor-specific certificates (for all device types in the Local Cloud)
      That solution is not scalable or possible when there are more than one vendor of certificates in a Cloud.
  Solution is only adequate when a specific certificate hierarchy is implemented:
    There is a root of trust („cloud certificate”) in which all Systems trust
    Every AppSys certificate shall be signed by the Cloud cert.
    This way the trust stores can be set up properly.
    G3.2 implements this hierarchy  a specific BOOTSTRAP mechanism is required

## Slide 8: G3.2 security features and concepts

## Slide 9: G3.2 core interactions (in the most secure scenario: centralized session control)
Notes: Introduction and goals of AH
Local Clouds work in SOA.
There are the mandatory core systems, that offer basic governance.
Authorization now bears two tasks: access control information, token gen.
SR: now capable of cleaning up the database, implements service metadata with every offering separately.
Gatekeeper has two services: GSD, ICN.
Network Manager will be required to build up inter-cloud data end-to-end path.

## Slide 10: G3.2 uses X.509
Private and Public keys (PKI!)
Trust stores and key stores within Systems set up in an Arrowhead way
Arrowhead Chain of Trust; Local Certificate Agents;
AH Master CA
Cloud 1 CA
Cloud 2 CA
System A Certificate
System B Certificate
System M Certificate
…
System N Certificate
System O Certificate
System X Certificate
…
- May be self-signed

## Slide 11
AH Master CA
Cloud 1 CA
Cloud 2 CA
System A Certificate
System B Certificate
System M Certificate
…
System N Certificate
System O Certificate
System X Certificate
…
May be self-signed or issued by e.g. Verisign
Managed by the AH consortium
Certificate structure implemented within G3.2
Issued by the consortium when a new Local Cloud is deployed
Issued by the local Authorization System upon BOOTSTRAPPING

## Slide 12: Certificate structure implemented within G3.2
Application
Authorisation
Authentication
Transport
Notes: A Sys & Service hierarchiához illeszkedően definiáltuk az X.509 cert struktúrát.
Ezt a CN-ben implementáltuk és az Authorization System-re bíznánk a CA feladatkört. Jelenleg azonban manuális cert generálás van, mert ez egy bootstrapping folyamat része.
Implementation benefits

## Slide 13: Transport level AA
All Core Systems implement:
  Can check the inbound certificate
  Is it signed by the Local Cloud certificate (trust store)?
    If yes: it belongs to the LC (can interact with theCore Systems)
    If no: it doesn’t belong to the LC (rejected)
  Can only register to Service Registry if belongs to the LC
    Using the G3.2 SR REST-based bridge towards the DNS-SD
  Can only request Orchestratrion if belongs to the LC
All Systems should implement:
  Check the Core Systems’ identity upon connection
    No one should be able to pose as the Orchestrator
  Can be done using the CN field
  Can be certain if the partner’s certificate is signed by LC cert

## Slide 14: Authorization System
The Authorization System stores public keys for all App. Systems
  Within the AuthenticationInfo field; Base64 encoding of 2048 byte PublicKey
Using 2048 bit certificate  244 bytes of token can be encrypted using simple RSA
  Decryptable by on the System it was intended for
  Since it is encrypted using its public key (decryptable by private one)
It is generated during the orchestration process
  As a final step; after Consumer – Service – Provider trio has been set
  By the local Authorization System, and based on the access rights stored in the database

## Slide 15: Authorization System
  In the future the Authorization System shall act as a Local Certificate Agency
  There shall be a bootstrapping mechanism in which the „waking up” System gets its runtime configuration after identity verification.
    This shall include the issue of an Arrowhead local runtime certificate.
    The System should use this in its communications with the Core Systems.
    All before-mentioned security solutions rely on this process.
  With all CA functionalities (cert issue, revoke, validation), the AA System

## Slide 16: The token itself
Two fields (SHA1withRSA; Base64)
  Encrypted JSON (<=244 bytes)
  Signature of the local Authorization System
Token Generation Service
Orchestrator
Authorization

## Slide 17: RawTokenInfo
cipher = Cipher.getInstance("RSA/ECB/PKCS1Padding");
The encoded JSON:
  {
  „c”:”<SystemName>.<SystemGroup>.<CloudName>.<Operator>”,
  „s”:”<interface>.<ServiceName>.<ServiceGroup>”,
  „e”:”<endTimeInEpoch>”,
  }
public class RawTokenInfo
  {
  private String s;
  private String c;
  private Long e;
  }

## Slide 18: Token in the local orchestration process

## Slide 19: Token when no orch. process implemented

## Slide 20: Security IN the Service and NOT AS a Service
Within the Application Service,
not defined by Arrowhead frame (how it is implemented within)!
It can be implemented for example:
Simple request-response cases (e.g. for REST)
  As a request path parameter (as currently implemented)
    GET to: /temperature&token=<value>&signature=<value>
    if (consumer.equals(consumerWithToken)) {
    if (endTime == 0L || (endTime > currentTime)) {
    AllowConsumption();
    }}
  Within the HTTP header
    Same concept

## Slide 21: Consumer – Provider handshake
2. Persistent connection setup (e.g. Websocket)
  Same as REST, in the initial connection shall contain these params
3. Publish-subscribe (MQTT, AMQP, OPC-UA)
  The serviceURI can be a topicname.
  The token handling is not defined yet.
    Can be in the topic name or during a handshake

## Slide 22: The Orchestrator/Consumer will know…
Service instances that implement various security measures shall have this information submitted to the SR as metadata.
  „security” = „SSL”
  „token” = „required”
  Via the secure REST interface
Orchestration Process: If the Orchestrator fetches a Service Provider with a Service that contains these metadata descriptors is will automatically.
No orch. proc. Implemented: When the Consumer looks up the Provider, it can also detect these key-values.

## Slide 23: Inter-Cloud orchestration with the token
Orchestrator
Gatekeeper
Gatekeeper
Orchestrator
Authorization
A
B
1
2
3
4
5
Gateway
Gateway
Consumer
Service Provider
7
7
8
9
10
10
10
9

## Slide 24: Benefits of this solution
Existing standard and implementation; core of the Internet
Chain of trust model  can be mapped to AH hierarchy
Assimetric key criptography
  Assures confidentiality, integrity and authenticity of messages at the same time
Identity of a System is connected to its certificate.
Provider doesn’t have to know consumer previously
  only have to trust the Authorization System of its Local Cloud
Authentication information can be extracted from the inbound client’s certificate
Can be used for authorization
  Token generation
  Which can also include logging (Accountability)

## Slide 25: Benefits of this solution II.
Security within Services: handshake between Consumer and Provider
The token verifies that proper orchestration took place. Not an ad hoc connection attempt in the network (or malicious).
During the creation of the token:
  Security logs can be made
  Additional (e.g. billing related) services can be utilized.

## Slide 26
Usage of SSL is also not mandatory.
The token generation is not mandatory. Not all Services have to implement.
Secure and insecure Services can co-exist in an LC.
  The Orchestrator knows will know from Service metadata when to force token generation and when not to bother.
There can be a secure (port 8080) and insecure (8443) Orchestrator instance as one entity for Systems of different security capabilities (resources).
  The Orchestration service is stateless.
The token generation then can be triggered by:
  The consumer (who knows that the Service type is a secure one, needs token to access it)
  The Orchestration Store (future work) can contain this flag.
Benefits of this solution III.

## Slide 27
Bootstrapping process can be established
  When new Systems are created and introduced to the LC
  Automatic certificate generation and distribution
Inter-Cloud AAA is possible.
Gives us the possibility to govern how Local Clouds are established
  LC certificate can only be issued by the Master Arrowhead CA
  Which can be the consortium
Benefits of this solution IV.

## Slide 28: Shortcomings / future work
Currently System certificates are generated manually
X509 certificates are based on PKI
Private key encryption (SSL) is resource demanding as is
There are several extensions / alternative solutions:
  Lightweight certificates for sensor nodes
  Elliptic Curve Cryptography (ECC) instead of RSA
  Variable key security authentication
  Standard and widely used protocols: Oauth with OpenID Connect
  TODO
Vendor issued cert integration (vs. Bootstrapping)

## Slide 29: Future work I.
Bootstrap mechanism
  When a System first connects to the Local Cloud it shall be authenticated and authorized into the Cloud.
  This can happen either with design-time allocation of Arrowhead-issued certificates
  Or during an automated bootstrapping.
    Using the original, vendor-issued certificate of the device
      This can be even stored in a trusted platform module (TPM)
    This certificate can be validated by a cooperation between:
      System and Device Registries
      Authentication System (Certificate Authority of the Local Cloud)
  In the end of this process:
      The vendor certificate shall be verified and identity confirmed (authentication INTO the LC)
      System configuration shall be downloaded and System shall be ready to start
      An Arrowhead runtime certificate shall be issued for the System which can be used to access other Core Systems and Application Systems.

## Slide 30: Future work II.
Accounting
  During token generation additional functionalities can be added.
    Logging or financial services (e.g. payment services).
  Since the token generation is a „symbol” for session establishment.
  Here we need:
    Security logging in the Core
    Security logging by the Provider
    Financial recording of the Service transaction.

## Slide 31: ?
Thank you!
hegeduscs@aitia.ai